## Slide 1: Machine Learning Aboard the ADAPT Gamma-Ray Telescope
By: Ye Htet (Presenter), Marion Sudvarg, Andrew Butzel, Jeremy D. Buhler, Roger D. Chamberlain, and James H. Buckley
This work was supported by NASA award 80NSSC21K1741, an NSF REU site award and by Washington University seed grant CC0001285 (PJ000030737)

## Slide 2: Introduction
Determining the nature of dark matter
Understanding energetic transient events in the deep universe
APT: Advanced Particle-astrophysics Telescope

## Slide 3: Introduction
Balloon demonstration of the components and detectors (smaller)
Launching in late 2025
ADAPT: Antarctic Demonstrator for APT

## Slide 4: Introduction
Determining the source of Gamma Ray Bursts
Typically last a few minutes (Long GRBs) but there are many <2 seconds (Short GRBs)
Signal other telescopes to point towards the source (Multi-messenger)
Gamma-Ray Burst (GRB) Localization
GRB 190114C Caption: New observations from NASA's Hubble Space Telescope have investigated the nature of the powerful gamma-ray burst GRB 190114C by studying its environment. Credits: NASA, ESA, and M. Kornmesser

## Slide 5: Motivation
Multiple instruments over different wavelengths for fast follow up analysis.
Many instruments perform omnidirectional event detection but use compute-intensive pattern-matching searches.
Must run on large clusters.
ML and Multi-messenger astrophysics

## Slide 6: Motivation
Deep Learning approach has been promising for processing large data efficiently and accurately.
In gravitational-wave astronomy, neural networks detect transient events
  can process months of data from the LIGO detector within 50 second.
Still deployed on ground-based computers.
ML and Multi-messenger astrophysics

## Slide 7: Motivation
Pipeline that runs onboard the telescope, for fast follow up analysis.
Non-machine learning approach currently works for APT (sub-degree error) but for ADAPT(balloon) suffers from additional noise and smaller component.
New machine learning approach that can work in conjunction with the traditional approach that improves accuracy while within timing deadline.
Our Goal

## Slide 8: Contribution
Apply two neural networks (Multi-Layer Perceptrons) to the GRB localization problem
  Background/signal identification (Classification)
  Uncertainty estimation (Regression)
Quantization and FPGA deployment
Machine Learning Approach

## Slide 9: Outline
Background
  GRB localization pipeline
Neural Networks
Localization Results
  Accuracy
  Speed
Quantization, FPGA

## Slide 10: GRB Localization Pipeline
MeV range Gamma-ray Telescopes (Compton)

## Slide 11: GRB Localization Pipeline
MeV range Gamma-ray Telescopes (Compton)
ŝ

## Slide 12: GRB Localization Pipeline
Reconstruction
Localization
  Approximation
  Iterative Refinement

## Slide 13: GRB Localization Pipeline
Determine the first two hits and the energy of the gamma-ray
Reconstruction

## Slide 14: GRB Localization Pipeline
Determine the first two hits and the energy of the gamma-ray
Reconstruction Result: A Compton ring that is a prediction for source of the gamma-ray
Reconstruction
η

## Slide 15: GRB Localization Pipeline
Approximation
  Sample some rings and get initial source estimate of maximum likelihood given rings
  Use dEta as weights
Refinement
  Select rings close to the initial estimate
  Iteratively apply least squares
  Use dEta as weights
Localization

## Slide 16: Machine Learning: Neural Networks
Earth's atmospheric particle background
Two challenges for ADAPT

## Slide 17: Machine Learning: Neural Networks
Earth's atmospheric particle background
Two challenges for ADAPT
Background Gamma-rays
Background Particles
(Neutrons + Electrons + Protons)

## Slide 18: Machine Learning: Neural Networks
Two challenges for ADAPT
Earth's atmospheric particle background
Large quantities of background rings generated from reconstruction
2-3x as many as “source” rings

## Slide 19: Machine Learning: Neural Networks
Earth's atmospheric particle background
Better quantification of uncertainty (dη)
  Traditionally, by propagation*
  Used as weights in localization
Two challenges for ADAPT
*Y. Htet, M. Sudvarg, J. D. Buhler, R. D. Chamberlain, and J. H. Buckley, “Localization of gamma-ray bursts in a balloon-borne telescope,” in Proc. Wkshps. Int’l Conf. High Performance Computing, Network, Storage, and Analysis (SC-W), Nov. 2023, pp. 395–398.
Y. Htet et al., “Prompt and accurate GRB source localization aboard the Advanced Particle Astrophysics Telescope (APT) and its Antarctic Demonstrator (ADAPT),” in Proc. 38th Int’l Cosmic Ray Conf., vol.444, Jul. 2023, pp. 956:1–956:9

## Slide 20: Machine Learning: Neural Networks
Earth's atmospheric particle background
  Background filter network (Classification)
Better quantification of uncertainty (dη)
  dEta network (Regression)
Two challenges for ADAPT

## Slide 21: Neural Networks
Model Usage
Extend our original pipeline
Still use the same two stages

## Slide 22: Neural Networks
Model Usage
Remove background rings using Background network
Refine rings with dEta network
Once final localization stage

## Slide 23: Neural Networks
Inspired by (Takashima, 2022)*
Made of blocks
Hyperparameter tuning
  Width
  Depth
  Shape
Model Architecture
*S. Takashima, H. Odaka, H. Yoneda, Y. Ichinohe et al., “Event reconstruction of compton telescopes using a multi-task neural network,” Nucl.
Instrum. Methods Phys. Res. A, vol. 1038, p. 166897, 2022.

## Slide 24: Neural Networks
13 Features
First 2 hits (Hit 0, Hit 1) [5 x 2]
Gamma-ray Energy [2]
Estimate source vec*[1]
Input Features

## Slide 25: Experiments
Approximate a typical GRB using physics simulator (GEANT4)
Sampling 44600 gamma-rays
  1 MeV/cm2 fluence (GRB energy density)
1000 trials
  68/95% containments
10 meta trials
  95% confidence intervals
Setup
68%
95%

## Slide 26: Experiments
Localization Accuracy
Approximate a typical GRB using physics simulator (GEANT4)
Sampling 44600 gamma-rays
  1 MeV/cm2 fluence (GRB energy density)
1000 trials
  68/95% containments
10 meta trials
  95% confidence intervals

## Slide 27: Experiments
Intel Atom CPU
  4 cores
  8GB RAM
  ~ 200 ms
Mean of 300 trials
Localization Speed

## Slide 28: Quantization
Can we further improve our latency?
Many model compression techniques:
  Pruning
  Knowledge Distillation
Quantization -> can be optimized for low-bit operators in hardware (size, speed, power)
Motivation

## Slide 29: Experiments
PyTorch's Eager Mode Quantization Aware Training (QAT)
'x86' default configuration
FP32 to INT8
68% containment is similar, but the 95% containment got worse
Quantization

## Slide 30: Experiments
High Level Synthesis tool (Vitis HLS)
Pipelined execution of layers
For 597 rings (1 MeV/cm2) ~4 ms compared to 14-15 ms on the Atom
1.75× the throughput of FP32 on the FPGA
FPGA using HLS

## Slide 31: Conclusion
Neural network models improves resilience to background radiation and measurement uncertainty, under low-resource, real-time computation.
Preliminary evidence to support further resource reduction through quantization and acceleration in FPGA logic.
ADAPT, with ML, is expected to localize a moderately bright, short-duration GRB in under a second with a typical localization accuracy of six degrees (6°).

## Slide 32: Future Work
Consideration of additional sources of error, such as multiple events arriving simultaneously
More quantization strategies, including different configs and other libraries outside of PyTorch.
Finally, we will study the impact of our models on the full APT instrument which could allow localization of even dim (< 0.1 MeV/cm2) GRBs to within a degree or less.

## Slide 33: Machine Learning: Neural Networks
Earth's atmospheric particle background
Better quantification of uncertainty (dη)
  Used as weighting in localization
Two challenges

## Slide 34: Background
Gamma-Ray Localization Pipeline
Two stages
Reconstruction:
  Per gamma-ray
Localization
  Per batch of gamma-rays

## Slide 35: Gamma-Ray Localization Pipeline
Crystal emits light when gamma-ray (event) scatters within it.
We measure positions and energies of the interactions (hits).
Result: [(ri=(xi,yi,zi) , Ei)].
In general: Compton Telescope
Reconstruction
Crystal Layer
Fibers

## Slide 36: Gamma-Ray Localization Pipeline
Reconstruction
Hits appear simultaneous
Determine the first two hits and the energy
Reconstruction Result: A Compton's ring that is a prediction for source of the gamma-ray

## Slide 37: Gamma-Ray Localization Pipeline
If we know first two hits, Compton's law will tell us the direction of the source
But hits appear simultaneous
Algorithm infers hit order
Reconstruction Result: A Compton's ring that is a prediction for source of the gamma-ray
Reconstruction

## Slide 38: Neural Networks
Hyperparameter tuning using random grid search
Model Training

## Slide 39: Experiments
Varying fluences
1000 trials
  68/95% containments
10 meta trials
  95% confidence intervals
Localization Accuracy

## Slide 40: Experiments
High Level Synthesis tool (Vitis HLS)
Pipelined execution of layers
For 597 rings (1 MeV/cm2) 4.13 ms
(compared to 22-58 ms on the RPi 3B+ and 14-15 ms on the Atom), and achieves 1.75× the throughput of FP32
FPGA using HLS

## Slide 41: Experiments
If we know first two hits, Compton's law will tell us the direction of the source
But, hits appear simultaneous
Algorithm infers hit order
Reconstruction Result: A circle that is a prediction for source of the gamma-ray
Robustness

## Slide 42: Experiments
If we know first two hits, Compton's law will tell us the direction of the source
But, hits appear simultaneous
Algorithm infers hit order
Reconstruction Result: A circle that is a prediction for source of the gamma-ray
Polar vs Nopolar

## Slide 43: Experiments
PyTorch's Eager Mode Quantization Aware Training (QAT)
'x86' default configuration
FP32 to INT8
68% containment is similar, but the 95% containment got worse
Quantization