## Slide 1: Localization of Gamma-ray Bursts in a Balloon-Borne Telescope
Ye Htet, Marion Sudvarg, Jeremy Buhler, Roger D. Chamberlain, James H. Buckley
Funded by: NASA award 80NSSC21K1741

## Slide 2: APT: Advanced Particle-astrophysics Telescope
Why APT?
Determining the nature of dark matter
Understanding the physics of neutron-star mergers

## Slide 3: ADAPT
Antarctic Demonstrator for the Advanced Particle-Astrophysics Telescope (ADAPT)
Balloon demonstration of the components and detectors (smaller)
Launching in late 2025

## Slide 4: Gamma-Ray Burst (GRB) Localization
Determining the source of Gamma Ray Bursts
Typically last a few minutes (Long GRBs) but there are many <2 seconds (Short GRBs)
Signal other telescopes to point towards the source (Multi-messenger)
Credit:ESA/Hubble, M. Kornmesser

## Slide 5: Gamma-Ray Burst (GRB) Localization
Goal:
We want to localize the source to within 1 degree of arc in the sky
Motivation:
Other telescopes have narrow field of view (FOV)
Omnidirectional detectors (GW/Neutrino detectors) are computationally intensive
Every small degree matters!

## Slide 6: Gamma-Ray Burst (GRB) Localization
Goal:
We want the computation to be fast (sub-second) on a low power platform (limited resources)
Motivation:
Short GRBs last <2s
Other telescopes take some time to move and/or point

## Slide 7: Gamma-Ray Burst (GRB) Localization
Multi-messenger astrophysics
Gamma-ray detection can achieve
  better localization accuracy
  in shorter time using lower computation power
Post-detection impacts HPC taking place in other detectors
  E.g. Pattern matching (resource intensive)

## Slide 8: Contributions
Impact of Uncertainty in Spatial and Energy Measurements
Impact of other types of noise
Techniques to mitigate their effects

## Slide 9: Outline
Brief overview of the GRB localization pipeline and sources of noise and uncertainty
Using additional detector hardware to improve localization accuracy
Mitigating the impact of Atmospheric Particle Background
Localization results at varying incident angles of a GRB

## Slide 10: Pipeline
Detection
Reconstruction
Localization
Crystal emits light when gamma-ray (event) scatters within it
We measure positions and energies of the interactions (hits)
Result: [(ri=(xi,yi,zi) , Ei)]
Crystal layer
Fibers

## Slide 11: Pipeline
Detection
Reconstruction
Localization
If we know first two hits, Compton's law will tell us the direction of the source
But, hits appear simultaneous
Algorithm infers hit order
Reconstruction Result: A circle that is a prediction for source of the gamma-ray
θ
c
s

## Slide 12: Pipeline
Detection
Reconstruction
Localization
Intersect Compton rings from hundreds or thousands of events to infer a common source direction for the GRB.
Detector
GRB Source
Angular Error
s
v

## Slide 13: Noise and Uncertainty
Physical phenomena
  Gamma-ray leaving the detector
  Non-Compton phenomena
  Atmospheric particle background
  Incident angle of the GRB
Detector Noise (Sudvarg 2023*)
  Electronic Noise
  Detection efficiencies
Leads to missing/extra hits, incorrect energy measurements
*Marion Sudvarg, et al. “Front-End Computational Modeling and Design for the Antarctic Demonstrator for the Advanced Particle-astrophysics Telescope.” In Proc. of 38th International Cosmic Ray Conference – PoS(ICRC2023), volume 444, pages 764:1–764:9, July 2023.

## Slide 14: Experiments
GEANT – A physics simulator (CERN)
  Physical Phenomena Noise
Gives us extra information about the events (Ground truth(GT) hit energies and positions)
We implement a device simulation ("Measured" values of the hits (ri, Ei))
  Detector Noise
Physics Simulation
(GEANT)
Detector Simulation
GT + "Physics" Noise
Complete Noise: (ri, Ei)

## Slide 15: Using additional detector hardware to improve localization accuracy

## Slide 16: Energy vs Spatial Measurements
Input: [(ri, Ei)]
Goal: Where is the weak link?
Experiment: Use ground truth information from the physics simulator (GEANT)

## Slide 17: Energy vs Spatial Measurements
Experiment: Swapping Ground Truth values
Data | Energies | Positions (Spatial)
1 | Measured | Measured
2 | Measured | Ground Truth
3 | Ground Truth | Measured
4 | Ground Truth | Ground Truth

## Slide 18: Energy vs Spatial Measurements
Approximate a typical GRB
Sampling 18700 events
  1 MeV/cm2 fluence (GRB energy density)
1000 trials
  68/95% containments
10 meta trials
  95% confidence intervals
P% Containment: P% of the trials are less(better) than that value
Detector
GRB Source
Angular Error
s
v

## Slide 19: Energy vs Spatial Measurements
GT = Ground Truth
Approximate a typical GRB
Sampling 18700 events
  1 MeV/cm2 fluence (GRB energy density)
1000 trials
  68/95% containments
10 meta trials
  95% confidence intervals

## Slide 20: Edge Detectors & Tail Counters
Edge Detector
At the side of the device layers
Provides a better energy estimate of each hit
Tail Counters
At the bottom the device
Provide a better total energy estimate of the whole gamma-ray

## Slide 21: Edge Detectors & Tail Counters
Approximate a typical GRB
Sampling 18700 events
  1 MeV/cm2 fluence (GRB energy density)
1000 trials
  68/95% containments
10 meta trials
  95% confidence intervals

## Slide 22: Mitigating the impact of Atmospheric Particle Background

## Slide 23: Atmospheric Particle Background
ADAPT's balloon instrument will be flying in the Earth's atmosphere
Atmospheric background particles appears as extraneous events in our computational pipeline
May be reconstructed to different directions other than the source

## Slide 24: Two Strategies for Removing Background
Remove events in which two hits occur in the same layer
Rejects reconstructed events for which the Compton ring lies entirely below the horizontal

## Slide 25: Atmospheric Particle Background

## Slide 26: Localization results at varying incident angles of a GRB

## Slide 27: Final Localization Accuracy
The error broadly increases with increasing angle
is within 2-3 degrees of accuracy for ≤ 40° incident angles

## Slide 28: Final Localization Accuracy
Achieved significant improvement in accuracy
Not <1 degree?
  We are using a smaller detector for ADAPT
  APT will have 45 times larger area – significant improvement in accuracy

## Slide 29: Conclusion & Future Direction
GRB Localization for ADAPT
  is within 2-3 degrees of accuracy for ≤ 40° incident angles
  68% of the time
  on the smaller detector,
  and in the presence of background radiation in the upper atmosphere
Extending the work to full APT
Considering additional sources of uncertainty
  Bandwidth of electronics reducing the effective number of photons available